## Slide 1: CCUS The Energy Council December 6, 2024

## Slide 3: What is CO2?
Carbon dioxide (CO2) is an inert gas that occurs both naturally and as a byproduct of industrial processes such as:
  Production of ethanol and hydrogen
  Combustion of coal, natural gas, gasoline and other carbon-based fuels
CO2 is being emitted into the atmosphere at record levels
CO2 is non-flammable and non-combustible

## Slide 4
There are a number of factors that Tenaska considers when siting a CCS project, including:
  Geology that provides access to safe and secure CO2 storage
  Regions that have a high concentration of emissions sources
  Communities that are welcoming to the economic benefits
Where can we store CO2?

## Slide 5: What is Pore Space?
Pore space is the empty space within and between rocks, similar to holes in a sponge
When we consider the appropriate geology for a CCS project, we look for porosity and permeability of the pore space
Notes: The types of rock that are well suited for CO2 storage are sandstone and dolomite. These rocks, in essence, absorb the CO2 like sponge. Another important factor is a thick layer of caprock, such as shale or evaporite/salt-, that seals the top of the porous rock, creating an impermeable barrier that prevents the stored CO2 from migrating upward. Together – the porous rock and the caprock – create an all-natural storage space. This region has sufficient porous rock – with the right combination of porosity and permeability – overlaid with caprock to support a CCS project.

## Slide 6: Where is the pore space?
Liquefied CO2 is deposited into “pore space” in the geologic formations deep, deep underground

## Slide 7: What is the CCS value chain?
CCS captures CO2 emissions produced by manufacturers and industrial facilities before they enter the atmosphere
Captured CO2 is liquified, transported and permanently stored deep underground beneath a thick layer of impermeable cap rock
CO2 then naturally mineralizes and dissolves over time

## Slide 9: What is the opportunity?